## Slide 1: Lecture 2b
Beer’s Lambert Law

## Slide 2: Electromagnetic Spectrum
Electromagnetic Spectrum
Visible range: l=380-750 nm
Ultraviolet: l=190-380 nm
Low energy
High energy

## Slide 3: Emission vs. Absorption
When determining a color, one has to know if the process that causes the color is due to emission or due to absorption of electromagnetic radiation.
Example 1: Sodium atoms emit light at l=589 nm resulting in a yellow-orange flame.
Example 2: Indigo absorbs light at l=605 nm that | is in the orange range  the compound assumes the complementary color (blue-purple)

## Slide 4: Beer’s Law
Fundamental law regarding absorbance of electromagnetic radiation:
The cell dimension (l) is usually 1 cm (for standard cuvettes).
The e-value is wavelength dependent. Thus, a spectrum is a plot of the e-values as the function of the wavelength (unit for e: M-1*cm-1).
The larger the e-value is, the larger the peak is going to be.
The data given in the literature only list the wavelengths and e-values (or its log value) of the peak maxima i.e., 331 (6460 or 3.81).
The desirable concentration of the sample is determined by the largest and smallest e-values of the peaks in the spectral window to be measured.

## Slide 5: Practical Aspects
The absorbance readings for the sample have to be in the range from Amin=0.1 and Amax=1 in order to be reliable.
Concentration limitations are due:
  Association at higher concentrations (c>10-4 M)
  Linear response of the detector in the UV-spectrophotometer
Linear range for absorbance
Concentration
Absorbance
0.1
1.0
cmin
cmax
Linear concentration range

## Slide 6: Iron Determination I
The reaction of Fe2+-ions with bipyridyl (2,2’-bipyridine) leads to the red-violet complex.
The complex is chiral and consists of equal amounts of the D- and L-isomer.
Note that only Fe2+-ions form the complex but not Fe3+-ions (l=620 nm, e=220). Thus, any Fe3+-ions have to be reduced first (with ascorbic acid) prior to the measurement.
The absorbance of the sample (via the transmission) at the wavelength of l=520 nm (e= ~8660) can be used to determine the concentration of the Fe2+-ions in solution.

## Slide 7: Iron Determination II
However, the proper response has to determined first by using standards to establish a calibration curve:
  The student prepares several Fe2+- solution with known concentration and obtains the absorbance readings for the Fe2+-complex.
  It is important to blank the spectrophotometer before each measurement (Why?).
  The slope of the best-fit line (Absorbance vs. concentration) should be close to the molar extinction coefficient.