## Slide 1: Lecture 5a
Recrystallization

## Slide 2: Introduction
Purification Techniques
  Distillation: liquids, gases, some solids
  Sublimation: solids only
  Recrystallization: solids mainly
  Chromatography: solids, liquids, gases
  Extraction: mainly liquid-liquid (often involves acid-base chemistry), sometimes solid-liquid
  Zone melting i.e., purification of silicon, etc.

## Slide 3: Theory of Recrystallization I
Dissolution
  Breaking solute-solute attractions (endothermic)
  Breaking solvent-solvent attractions (endothermic)
  Forming solvent-solute attractions during the solvation process (exothermic but with varying degrees depending on the type of interaction)
  Most dissolution processes of organic compounds are endothermic unless strong bonds (i.e., hydrogen bonds) are formed between the solute and the solvent.
Precipitation
  This step requires the loss of the solvent cage (endothermic)
  Ordered packing of the target compound (exothermic)
DH(sol)

## Slide 4: Theory of Recrystallization II
Three basic scenarios are possible for the solution behavior (the graphs are linear to show the trends only)
  Case 1: The compound dissolves poorly at all temperatures 
  Case 2: The compound dissolves well at all temperatures 
  Case 3: The compound dissolves well at high temperatures but poorly at low temperatures 
Solubility
Temperature

## Slide 5: Theory of Recrystallization III
How do we pick a solvent?
  Goal: the target compound should exhibit a steep solubility curve in the solvent (case 3), while the impurity (ideally) dissolves well at all temperatures (case 2)
  The recrystallization solvent has to have a somewhat different polarity compared to the target compound but ideally be similar to polarity of the impurity (“Like-dissolves-like”)
  Example 1: Separation of benzil (weakly polar) and benzoin (medium polar)
    To isolate benzil: 95 % ethanol, methanol
    To isolate benzoin: benzene, CCl4

## Slide 6: Theory of Recrystallization IV
Solvent mixtures
  They will be used if a single solvent is not available for recrystallization
  They allow to fine-tune solubility behavior (i.e., steepness of curve)
  The composition of the mixture will change if the mixture is boiled too long because the lower boiling solvent will evaporate
Example 2: TPCP (weakly polar)
Toluene (b.p.= 111 oC)
95 % ethanol (b.p.= 78 oC)
Solubility
Temperature
Toluene: 95 % ethanol (1:1)
Toluene: 95 % ethanol (2:1)
impurity

## Slide 7: Procedure I
Place the crude solid in an Erlenmeyer flask of proper size
Add a small amount of the cold solvent to the solid
Add a spin bar or boiling stick to the suspension
Place a watch glass with some ice cubes on the top
Heat the mixture to a gentle boil
Why is this important?
How much solvent should be added?
Why are they added?
Why is the watch glass placed on the top?
What is the student looking for?
To minimize the loss of solvent and target compound
To avoid bumping
About half of what was calculated
To condense the solvent
The entire crude dissolves

## Slide 8: Procedure II
After the entire solid is dissolved, remove the flask from the hotplate
Allow the saturated solution to cool down to room temperature slowly
Place the solution/mixture in an ice-bath
Isolate the crystals by vacuum filtration
Rinse the crystals with a small amount of ice-cold solvent
Why is it important that the entire solid dissolved?
Why is the solution cooled down slowly?
Why is the mixture place in an ice-bath?
Review vacuum filtration
How much is appropriate here?
To dissolve the impurities
To obtain better quality crystals

## Slide 9: Troubleshooting
Which steps should be taken if no precipitates forms upon cooling?
  Remove some of the solvent
  Scratch the insides of the Erlenmeyer flask with a glass rod
  Add seeds crystals to the solution
  Add a solvent that lowers the solubility of the target compound and keeps the impurities in solution