## Slide 1: Lecture 4c
Extraction

## Slide 2: Why do we need Extraction?
Chemical reactions usually lead to a mixture of compounds: product, byproducts, reactants and catalyst
It is one way to facilitate the isolation of the target compound
  Extraction: aims at the target compound
  Washing: removes impurities from the organic layer

## Slide 3: Theory I
Extraction is based on the distribution of a compound between two phases i.e., aqueous and organic phase
Often this is accomplished by acid-base chemistry, which converts a compound into an ionic specie making it more water-soluble:
  Acidic compounds are removed by extraction with bases like sodium hydroxide or sodium bicarbonate
  Basic compounds are removed by extraction with mineral acids i.e., hydrochloric acid
  Polar compounds (i.e., alcohols, mineral acids) are removed by extraction with water i.e., small molecules (note that there will be a distribution between the organic and the aqueous layer)
  Non-polar molecules cannot be removed from the organic layer because they cannot be modified by acids or bases and do not dissolve in water well either
  Water is removed from the organic layer using saturated sodium chloride solution (bulk) or a drying agent (for smaller amounts of water)

## Slide 4: Theory II
If an organic compound is extracted from an aqueous layer or a solid, the chosen solvent has to meet certain requirements:
  The target compound should dissolve very well in the solvent at room temperature (“like dissolves like” rule applies)  a large difference in solubility leads to a large value for the partition coefficient (also called distribution coefficient), which is important for an efficient extraction
  The solvent should not or only slightly be miscible with “aqueous phase” to be extracted
  The solvent should have a low or moderately low boiling point for easy removal at a later stage of the product isolation

## Slide 5: Theory III
Removal of an Acid
  A base is used to convert the acid i.e., carboxylic acid into its anionic form i.e., carboxylate, etc., which is more water soluble
  Reagents: 5 % NaOH or sat. NaHCO3
  Recovery: The addition of a strong acid to the combined aqueous extracts allows for the recovery of the carboxylic acid, directly (i.e., precipitation of benzoic acid) or indirectly (i.e., extraction)
  Sodium hydroxide cannot be used if the target compound is sensitive towards strong bases i.e., esters, ketones, aldehydes, epoxides, etc.
  The use of sodium bicarbonate will produce carbon dioxide as byproduct if acids are present, which can cause a pressure build-up in the extraction vessel i.e., centrifuge tube, separatory funnel, etc.

## Slide 6: Theory IV
Removal of a Phenol (=weak acid)
  A strong base is used to convert the phenol into a phenolate, which is more water-soluble
  Reagent: 5 % NaOH
  Recovery: The addition of a strong acid to the combined aqueous extracts allows for the recovery of the phenol, directly (i.e., precipitation) or indirectly (i.e., extraction)
  Sodium bicarbonate is usually not suitable for the extractions of phenol because it is too weak of a base (pKa=6.37) to deprotonate weakly acidic phenols (pKa=10). The equilibrium constant for the reaction would be K=10-3.63=2.34*10-4 which means that only ~0.02 % of the phenol would be deprotonated by the bicarbonate ion.

## Slide 7: Theory V
Removal of a Base
  A strong acid is used to convert the base i.e., amine into its protonated form i.e., ammonium salt, which is more water-soluble
  Reagent: 5 % HCl
  Recovery: The addition of a strong base to the combined aqueous extracts allows for the recovery of the basic compound, directly (i.e., precipitation of lidocaine) or indirectly (i.e., extraction of 2,6-xylidine)

## Slide 8: Theory VI
The extraction process can be quantified using the partition coefficient K (also called distribution coefficient)
Using this partition coefficient, one could determine how much of the compound is extracted after n extractions
The formula illustrates several important points:
  A large value for K is favorable for an efficient extraction
  Multiple extractions with small quantities of solvent are better than one extraction with the same total volume
V1= volume of solvent to be extracted
V2= total volume of the extraction solvent
K= distribution coefficient
w0= amount of solute in solvent 1

## Slide 9: Theory VII
Partition coefficients are defined in different systems i.e., log Kow, which quantifies the distribution of a compound between octanol and water
  )
  A negative value means that the compound is polar and dissolves better in water than in octanol
Compound | Log Kow | Water solubility at 20 oC
Benzoic acid | 1.90 | Poorly (3 g/L)
Sodium benzoate | -2.27 | Highly (556 g/L)
Phenol | 1.46 | Soluble (83 g/L)
Sodium phenolate | -1.17 | Highly (530 g/L)
Triethylamine | 1.45 | Soluble (130 g/L)
Triethylammonium chloride | -1.26 | Highly (1370 g/L)

## Slide 10: Practical Aspects I
Solvent
  Solubility issue (water=W, solvent=S)
  The solubility of the solvent in aqueous solution is a reason for the requirement to use a minimum of 10-20 % of the volume for the extraction. Excessive amounts for one single extraction (>30 %) are wasteful and should be avoided
  Safety considerations
    Health hazards
    Flammability
    Environmental impact
Solvent | Log Kow | S in W | W in S | Flammable | Density
Chloroform | 1.97 | 0.8 % | 0.056 % | NO | 1.48 g/cm3
Dichloromethane | 1.25 | 1.3 % | 0.25 % | NO | 1.33 g/cm3
Diethyl ether | 0.89 | 6.9 % | 1.4 % | YES | 0.71 g/cm3
Ethyl acetate | 0.73 | 8.1 % | 3.0 % | YES | 0.90 g/cm3
Hexane | 3.90 | ~0 % | ~0 % | YES | 0.66 g/cm3

## Slide 11: Practical Aspects II
Equipment
  Which equipment should be used in this procedure depends on the volume of total solution being handle
    5 mL conical vial: V< 3 mL
    12 mL centrifuge tube: V< 10 mL
    Small separatory funnel (125 mL): V< 90 mL
    Larger separatory funnels are available (up to 25 L)
  Separatory funnels have to be checked for leakage on the top and the bottom before being used
  All extraction vessels have to be vented during the extraction because pressure might build up due to the exothermic nature of the extraction and/or the formation of a gas i.e., carbon dioxide.

## Slide 12: Practical Aspects III
Emulsion
  Excessive shaking
  It will be observed if the polarities and densities of the phases are similar
  If a mediating solvent is present i.e., ethanol, methanol, etc., which dissolves in both layers
  A precipitate forms during the extraction
  They can often be avoided by less vigorous shaking
Salting out
  Addition of a salt increases the polarity of the aqueous layer
    It causes a decreased solubility of many organic compounds in the aqueous layer
    It “forces” the organic compound into the organic layer because the polarity of the aqueous layer increased
    It can also causes a better phase separation

## Slide 13: Summary
If the correct solvent was used for extraction, 2-3 extractions are usually sufficient to isolate the majority of the target compound
Unless large amounts of material are transferred from one phase to the other, the solvent/solution volume that should be used for extraction should not exceed 10-20 % of the volume being extracted
In Chem 30BL and Chem 30CL, only non-chlorinated solvents i.e., diethyl ether (r= 0.71 g/mL), ethyl acetate (r=0.90 g/mL), etc. are used for extraction. Thus, the organic layer will usually be the upper layer because these solvents are less dense than aqueous solutions. A small amount of organic compound dissolved in the solvent does not change this!
The student has to always keep in mind that pressure will build up in the extraction vessel, particularly if sodium bicarbonate is used to extract acidic compounds
No extract should be discarded until the target compound has been isolated (and characterized!)