## Slide 1: Lecture 5a
Mass spectrometry

## Slide 2: History
J. J. Thompson was able to separate two neon isotopes (Ne-20 and Ne-22) in 1913, which was the first evidence that isotopes exist for stable elements (Noble Prize 1906 in Physics for the discovery of the electron in 1897)
F. W. Aston, who received the Noble Prize in Chemistry in 1922, discovered isotopes in a large number of nonradioactive elements by means of his mass spectrograph (first one build). He also enunciated the whole-number rule, which states that the masses of the isotopes are whole number multiples of the mass of the hydrogen atom
H. Dehmelt and W. Paul built the first quadrupole mass spectrometer in 1953 (Noble Prize 1989 in Physics)
K. Tanaka and J.B. Fenn developed the electrospray and soft laser desorption method, which are used for a lot of proteins (Noble Prize 2002 in Chemistry)

## Slide 3: Electron Impact Mass Spectrometry I
Electron Impact (EI) is hard ionization technique
  An ionizing beam of electrons generated in the ionization chamber causes the ionization and/or fragmentation of the molecule
  The higher the energy of the electrons is, the more fragmentation is observed up to the point where the molecular ion (M+) cannot be observed anymore
AB
AB
AB+
AB+
AB+
AB+
AB+
AB+
A+
A+
B+
B+
B+
From GC

## Slide 4: Electron Impact Mass Spectrometry II
  Mass spectrometers are often connected to gas chromatographs (GC/MS)
  They only require very small amounts of sample (~1 ng)
  The mass spectrometer employs an ultrahigh vacuum (<10-6 torr)
  Since there is only one detector, the magnetic field has to be scanned during the acquisition in order to collect ions with different m/z ratio, which arrive at different times
  The neutral fragments do not interact with the magnetic field and are lost in the process (bounce into the walls)

## Slide 5: Information from the Mass Spectrum I
The mass spectrum is a plot of the relative ion abundance versus m/z (mass/charge)
The molecular ion peak (=parent peak) is the peak that is due to the cation of the complete molecule
The base peak is the largest peak in the spectrum (=100 %)
Stevenson’s rule: When a fragmentation takes place, the positive charge remains on the fragment with the lowest ionization energy
  The more stable the fragment is, the higher the abundance of the ion is resulting in a larger peak because its lifetime is longer
  Commonly observed stable ions: m/z=43 (acylium or iso-propyl), m/z=57 (tert.-Bu or propylium), m/z=91 (benzyl), m/z=105 (benzoyl), etc.

## Slide 6: Information from the Mass Spectrum II
Molecular Mass
Presence of an odd number of nitrogen atoms (if molecular mass is odd)
The presence of certain fragments/groups gives rise to very peaks with a high abundance i.e., benzyl, acylium, etc.
Presence of certain functional groups result in characteristic fragments being lost (mass difference) or being observed i.e., alcohols exhibit a peak at m/z=31 due to [CH2OH]-fragment while at m/z=47 due to [CH2SH]-fragment

## Slide 7: Information from the Mass Spectrum III
Number of carbon atoms from the ratio of [M+1]/[M]-peaks (1.1 % for each carbon) i.e., the ratio would be 11 % (=0.11) if there were ten carbon atoms in the fragment
The McLafferty rearrangement is an intramolecular hydrogen transfer via a six-membered transition state from a g-carbon atom leading to a b-cleavage to the keto-group

## Slide 8: Information from the Mass Spectrum IV
If several chlorine and/or bromine atoms are present in the molecule, isotope clusters consisting of (n+1) peaks are found in the spectrum
Pattern for halogen clusters
Elements | X | X2 | X3
Cl | 100:32 | 100:64:10 | 100:96:31:3
Br | 100:98 | 51:100:49 | 34:100:98:32
Elements | Cl | Cl2 | Cl3
Br | 77:100:25 | 61:100:46:6 | 51:100:65:18:1.7
Br2 | 44:100:70:14 | 38:100:90:32:4 | 31:92:100:50:12:1

## Slide 9: Fragmentation I
Example 1: Butyrophenone (PhCOCH2CH2CH3)
m/z=148
(M+)
m/z=120
((M-C2H4)+)
m/z=105
((Ph-C≡O)+)

## Slide 10: Fragmentation II
Example 2: 1-Phenyl-2-butanone (PhCH2COCH2CH3)
m/z=148
(M+)
m/z=91
(PhCH2+)
m/z=57
(CH3CH2CO+)
No peak at m/z=120

## Slide 11: Fragmentation III
Example 3: 4-Phenyl-2-butanone (PhCH2CH2COCH3)
m/z=148
(M+)
m/z=43
(CH3CO+)
m/z=105
(PhCHCH3+)
m/z=91
(PhCH2+)

## Slide 12: Epoxide Analysis
Styrene oxide Phenylacetaldehyde Acetophenone
Differences
  m/z=91 ([C7H7]+): only found in phenylacetaldehyde and styrene oxide, but not in acetophenone
  m/z=105 ([C7H5O]+): only found in acetophenone!
  m/z=119 ([C8H7O]+): only found in styrene oxide!
  m/z=92 ([C7H8]+): due to McLafferty rearrangement!

## Slide 13: Chemical Ionization Mass Spectrometry I
Chemical Ionization is considered a soft ionization technique
  It uses less energy, which results in less fragmentation, allowing in many cases the observation of the molecular ion peak
  Methane (CH4), isobutane (C4H10) or ammonia (NH3) is used as gas
    Primary Ion formation: CH4 + e- CH4+ + 2e-
    Secondary Ion formation: CH4 + CH4+ CH5+ + CH3
    Product formation: M + CH5+ CH4 + [M+H]+ AH + CH3+ A+ + CH4
Chemical ionization can be performed in PCI (positive mode) or NCI (negative mode)
The NCI mode is used for PCBs, pesticides and fire retardants because they contain halogens with a high electronegativity, which makes the detection more sensitive for the compounds

## Slide 14: Chemical Ionization Mass Spectrometry II
Comparison of (a) EI, (b) PCI and (c) NCI for Parathion-ethyl (pesticide)
The EI spectrum shows significantly more fragmentation than the PCI and the NCI spectrum and therefore provides more structural information
EI: 291 [M]+, 109 [C2H5OPO2H]+ 137 [(C2H5O)2PO]+
PCI: 292 [M+H]+, 262 [M-C2H5]+
NCI: 291 [M]-, 154 (C2H5O)2PSH]- 169 [O2NC6H4O-]
EI
PCI
NCI