## Slide 1: Lecture 5b
Chromatography on Chiral Stationary Phases

## Slide 2: Introduction
Chiral stationary phase are used in gas-liquid chromatography (GC/GLC) and liquid-solid chromatography (HPLC)
Chiral GC columns are frequently used in pharmaceutical research (i.e., enantiomeric purity of drugs), quality control of nature products, forensics, etc.
Commonly used chiral stationary phases
  Amino acid derivatives i.e., Chirasil-Val
  Metal complexes i.e., L-hydroxyproline-Cu2+
  Carbohydrate derivatives i.e., cyclodextrins

## Slide 3: Cyclodextrins I
There are three commonly used cyclodextrins
 | a-form | b-form | g-form
Number of Glucose units | 6 | 7 | 8
Number of chiral centers | 30 | 35 | 40
External diameter (pm) | ~1420 | ~1530 | ~1720
Internal diameter (pm) | 470-520 | 600-650 | 750-850
Volume of cavity (nm3) | 0.176 | 0.346 | 0.510
Water solubility | 14.5 | 1.85 | 23.2
Melting or decomposition point (in K/oC) | 551/278 | 572/299 | 540/267
a
b
g

## Slide 4: Cyclodextrins II
The following interactions between an analyte and the cyclodextrin have an influence on the selectivity of the column:
  Inclusion which depends on the size of the substrate and the form of cyclodextrin (a, b, g)
  Dipole-dipole interactions which depends on the functional groups involved in the separation
  Hydrophobic interactions which is a function of the carbon content in the substrate
  Hydrogen bonds which depend on the functional groups and the substrate and the capping of the cyclodextrin
  Steric interactions: different enantiomers (diastereomers) interact differently

## Slide 5: Epoxide I
GC simulation (low tech!)
For some epoxides the major product elutes first and the minor product afterwards, in some cases it is the other way around (structure and temperature dependent)
The area of the peaks will be given on the printouts
  The e.e.-value can be calculated from the areas (B and C).
  Example: if peak B had an area of 100 units and peak C had an area of 45 units, the e.e.-value for the reaction would be 37.9 %.
alkene
epoxides
aldehyde/ketone
A
B C
D
Retention time
(min)
pA
Compound | b.p. (oC)
Styrene | 145
Styrene oxide | 192
Phenylacetaldehyde | 195
Acetophenone | 202

## Slide 6: Epoxide II
The two peaks that belong to the epoxides have identical mass spectra
The aldehyde/ketone peak has the same [M]+-peak but a different fragmentation pattern
Some of the aldehydes are chiral resulting in two peaks with the same area because the aldehyde mixture is racemic
The alkene peak show a [M]+-peak that is 16 amu lower than the ones above
Peaks that exhibit larger than [M]+-peak of the epoxide are usually due to chlorination products i.e., [M]:[M+2]+ = 3:1
Note that the chlorination products can be chiral as well, which means that they can exhibit more than one peak in the gas chromatogram (usually racemic)